## Slide 1: Going Faster
Performance in the Climb

## Slide 2: Agenda
When to Stop
Thermal Entry
Centring Technique
Efficient Exit
Flight Analysis
  Guy Corbett; Andy Roch

## Slide 3: Some General Points
Golden Rules of Climbing Well
  Fly Tight, Fly Slow, Fly Smooth
  Fly Really Smoothly, No Jerking About
  What not to do: follow this link
    Pudding stirring, jerking around the stick, holding it low down… I could go on
Get Into the Centre- use all the controls
  Use all the controls, but progressively; one smooth movement
  Use more control deflection if stronger, more turbulent
  Use less if weaker and smoother thermals
Speed and Pitch
  Modern, Heavy Gliders need to keep flying
  Dropping too slow hurts your climb a lot!
  Don’t hold back pressure and be super smooth in elevator

## Slide 4: Fly Smooth and Not Too Slow!
Allow the Air to stay attached
  Tight/Slow = smaller circle in best lift
  Also means nearer the stall or separation
  Big sharp control inputs result in break away
Smooth, Strong Thermals
  Get tight and hold the stick still
  Can get closer to the limits safely
Small Gusty Thermals
  If strong, tighten into the gusts
  If weaker, increase speed and open out- less critical
  Always keep enough speed to keep flying if you fall out

## Slide 5: When to Stop
Get out of Pavlovian Reflex
  Typical Turn is 20-30s
  Takes 7-12s to traverse the thermal straight
  Take your Time to slow and turn in!
  Manoeuvre harder for sharper changes in lift
Which Way to turn?
  Take your time- going the wrong way is EXPENSIVE
    20s in sink, correction turn, full circle to get back: 1-2Min?
  If in doubt- keep going straight! (take any excuse)

## Slide 6: Centring Technique
Visualise and Feel with Mark 1 Vario
  Respond to your seat, feel the aircraft, listen to airflow
  At peak, look along the outside wing- that is where it is
  At worst, look down the inside wing- MANOEVER THERE
Tighter or Open Turns to sneak up on it
  Simplest Approach: Roll Out- count to 3, Roll In
    Only if you have really lost the plot!
  Tighten as lift reduces
  Open turn as lift increases
  Hit best turn rate at peak lift
Use the Aircraft Capabilities
  LS7: massive roll rate, can but cant pull!
  Nimbus 4: huge ability to tighten into improving lift

## Slide 7: Nimbus 4 in weaker lift: open and tighten

## Slide 8: Nimbus in stronger lift: Wind it In!

## Slide 9: G9: Classic in, up and out into wind

## Slide 10: G9: Wrong Way!

## Slide 11: Exiting the Thermal
Look for the Exit Early
  Know your track at least 2-3 turns before the top
  Observe the cloud and plan for best air on exit
Judge when to leave
  Don’t Fixate: leave when you can do better within range
  Avoid: running off the edge at 100Kts to avoid cloud
  Try to: Leave earlier and bounce up to base
Speed On Before Sink
  Learn from previous clouds how hard to accelerate
  This will change from one leg to the next!
  Better to be faster in the lift and give away height
  Accelerate Before the Sink!

## Slide 12: Conclusions
Know your Aircraft
  Experiment with speeds and angles of bank and different weight
  Practice tighter, slower turns; find the limits for efficient climbing
  Aim for turns of 20-25s in good conditions, 30s in weaker thermals
Entering the Thermal
  Select candidates well ahead of time
  Approach slightly to one side, expecting to turn one way
  If you don’t hit it cleanly and positively- move on!
Centring
  Fly smooth, tight and not too slow
  Tighten turn in decreasing lift to cut time in weaker lift
  Open out turn in increasing lift to move to the centre
Exiting
  Plan ahead, find a good line and get speed on before the sink